Title
State Notation Language and the Sequencer
Andrew Johnson
APS Engineering Support Division
January 2007
USPAS EPICS Course

---
Outline
Outline
What is State Notation Language (SNL)
Where it fits in the EPICS toolkit
Components of a state notation program
Some notes on the Sequencer runtime
Building, running and debugging a state notation program
Additional Features
When to use it
This talk covers Sequencer version 2.0.8
This talk does not cover all the features of SNL and the sequencer. Consult the manual for more information:
  - http://www.slac.stanford.edu/comp/unix/package/epics/sequencer/

---
SNL and the Sequencer
SNL and the Sequencer
The sequencer runs programs written in State Notation Language (SNL)
SNL is a ‘C’ like language to facilitate programming of sequential operations
Fast execution - compiled code
Programming interface to extend EPICS in the real-time environment
Common uses
  - Provide automated start-up sequences like vacuum or RF where subsystems need coordination
  - Provide fault recovery or transition to a safe state
  - Provide automatic calibration of equipment

---
Where’s the Sequencer?
Where’s the Sequencer?
The major software components of an IOC (IOC Core)
LAN
Channel Access
IOC
Sequencer
Database
Device Support
I/O Hardware

---
Where’s the Sequencer Now?
Where’s the Sequencer Now?
Tools
MEDM
Client
Client
Client
MEDM
Sequencer
LAN
Server
IOC
IOC
IOC
Meter
Power Supply
Camera

---
The Best Place for the Sequencer
The Best Place for the Sequencer
Recent versions of the sequencer can be run either in an IOC or as a standalone program on a workstation
Traditionally sequencers run in the IOC
Locating them within the IOC they control makes them easier to manage
Running them on a workstation can make testing and debugging easier
On a workstation, SNL provides an easy way to write simple CA client programs

---
SNL implements State Transition Diagrams
SNL implements State Transition Diagrams
State A
Event
Transition
A to B
Action
State B

---
STD Example
STD Example
Start
Low vacuum
pressure < 5.1 uTorr
Open the valve
High vacuum
pressure > 4.9 uTorr
Close the valve

---
Some Definitions
Some Definitions
SNL : State Notation Language
SNC : State Notation Compiler
sequencer : The tool that executes the compiled SNL code
Program : A complete SNL application consisting of declarations and one or more state sets
State Set : A set of states that make a complete finite state machine
State : A particular mode of the state set in which it remains until one of its transition conditions is evaluated to be TRUE

---
SNL: General Structure and Syntax
SNL: General Structure and Syntax
program program_name
declarations
ss state_set_name {
  - state state_name {
  - entry {
  - entry action statements
  - }
  - when (event) {
  - action statements
  - } state next_state_name
  - when (event) {
  - ...
  - } state next_state_name
  - exit{
  - exit action statements
  - }
  - }
  - state state_name {
  - ...
  - }
}

---
SNL: General Structure and Syntax
program name	A program may contain multiple state sets. The program name is used as a handle to the sequencer manager for state programs.
ss name {	A state set becomes a task in the vxWorks environment.
state name {	A state is an area where the task waits for events. The related task waits until one of the events occurs and then checks to see which it should execute. The first state defined in a state set is the initial state.
option flag;	A state specific option
when (event) {	Defines the events for which this state waits.
} state next	Specifies the following state after the actions complete.
entry {actions}	Actions to do on entry to this state from another state. With option -e; it will do these actions even if it re-enters from the same state.
exit {actions}	Actions to do before exiting this state to another state. With option -x; it will do these actions even if it exits to the same state.

---
Declarations
Declarations – Variables
Appear before a state set and have a scope of the entire program.
Scalar variables
  - int	var_name;
  - short	var_name;
  - long	var_name;
  - char	var_name;
  - float	var_name;
  - double	var_name;
  - string	var_name; /* 40 characters */
Array variables: 1 or 2 dimensions, no strings
  - int	var_name[num_elements];
  - short	var_name[num_elements];
  - long	var_name[num_elements];
  - char	var_name[num_elements];
  - float	var_name[num_elements];
  - double	var_name[num_elements];

---
Declarations - Assignments
Declarations – Assignments
Assignment connects a variable to a channel access PV name
  - float pressure;
  - assign pressure to “CouplerPressureRB1”;
  - double pressures[3];
  - assign pressures to {“CouplerPressureRB1”, ”CouplerPressureRB2”, ” CouplerPressureRB3”};
To use these channel in when clauses, they must be monitored
  - monitor pressure;
  - monitor pressures;
Use preprocessor macros to aid readability:
  - #define varMon(t,n,c) t n; assign n to c; monitor n;
  - varMon(float, pressure, “PressureRB1”)

---
Declarations – Event Flags
Declarations – Event Flags
Event flags are used to communicate between state sets, or to receive explicit event notifications from Channel Access
Declare like this:
  - evflag	event_flag_name;
An event flag can be synchronized with a monitored variable
  - sync	var_name event_flag_name;
The flag will then be set when a monitor notification arrives
  - evflag	flag_monitor;
  - sync	pressure flag_monitor;

---
Events
Events
Event:	The condition on which actions associated with a when are run and a state transition is made.
Possible events:
Change in value of a variable that is being monitored:
  - when (achan < 10.0)
A timer event (not a task delay!):
  - when (delay(1.5))
  - The delay time is in seconds. It is declared internally as a double; constant arguments to the delay function must contain a decimal point.
  - A delay is normally reset whenever the state containing it is exited.
  - Use the state specific option -t; to stop it from being reset when transitioning to the same state.

---
Events (continued)
Possible Events (continued)
The state of an event flag:
  - when (efTestAndClear(myflag))
  - when (efTest(myflag))
  - efTest() does not clear the flag. efClear() must be called sometime later to avoid an infinite loop.
  - If the flag is synced to a monitored variable, it will be set when the channel sends a value update
  - The event flag can also be set by any state set in the program using efSet(event_flag_name)
Any change in the channel access connection status:
  - when (pvConnectCount() < pvChannelCount())
  - when (pvConnected(mychan))

---
Actions
Action Statements
Built-in action function, e.g. :
  - pvPut(var_name);
  - pvGet(var_name);
  - efSet(event_flag_name);
  - efClear(event_flag_name);
Almost any valid C statement
  - switch() is not implemented and code using it must be escaped.
  - %% escapes one line of C code
  - %{
  - escape any number of lines of C code
  - }%

---
Example - State Definitions and Transitions
Example – State Definitions and Transitions
Initial State
pressure > .0000051
      RoughPump on
      CryoPump off
      Valve closed
pressure <= .0000049
      RoughPump off
      CryoPump on
      Valve open
pressure <= .0000049
      RoughPump off
      CryoPump on
      Valve open
Low Vacuum
High Vacuum
pressure > .0000051
      RoughPump on
      CryoPump off
      Valve closed
10 minutes
      RoughPump off
      CryoPump off
      Valve closed
Fault

---
Example - Declarations
Example – Declarations
double pressure;
assign pressure to “Tank1Coupler1PressureRB”;
monitor pressure;
short	RoughPump;
assign RoughPump to “Tank1Coupler1RoughPump”;
short	CryoPump;
assign CryoPump to “Tank1Coupler1CryoPump”;
short	Valve;
assign Valve to “Tank1Coupler1IsolationValve”;
string CurrentState;
assign CurrentState to “Tank1Coupler1VacuumState”;

---
Example – State Transitions
Example – State Transitions, Actions Omitted
program vacuum_control
ss coupler_control
{
state init{
when (pressure > .0000051){
} state low_vacuum
when (pressure <= .0000049){
} state high_vacuum
}
state high_vacuum{
when (pressure > .0000051){
} state low_vacuum
}
state low_vacuum{
when (pressure <= .0000049){
} state high_vacuum
when (delay(600.0)){
} state fault
}
state fault {
}
}

---
Example – Init State
Example – Initial State
state init {
entry {
strcpy(CurrentState,”Init”);
pvPut(CurrentState);
}
when (pressure > .0000051){
RoughPump = 1;
pvPut(RoughPump);
CryoPump = 0;
pvPut(CryoPump);
Valve = 0;
pvPut(Valve);
} state low_vacuum
when (pressure <= .0000049){
RoughPump = 0;
pvPut(RoughPump);
CryoPump = 1;
pvPut(CryoPump);
Valve = 1;
pvPut(Valve);
} state high_vacuum
}

---
Example – State low_vacuum
Example – State low_vacuum
state low_vacuum{
entry {
strcpy(CurrentState,”Low Vacuum”);
pvPut(CurrentState);
}
when (pressure <= .0000049){
RoughPump = 0;
pvPut(RoughPump);
CryoPump = 1;
pvPut(CryoPump);
Valve = 1;
pvPut(Valve);
} state high_vacuum
when (delay(600.0)){
} state fault
}

---
Example – State high_vacuum
Example – State high_vacuum
state high_vacuum{
entry {
strcpy(CurrentState,”High Vacuum”);
pvPut(CurrentState);
}
when (pressure > .0000051){
RoughPump = 1;
pvPut(RoughPump);
CryoPump = 0;
pvPut(CryoPump);
Valve = 0;
pvPut(Valve);
} state low_vacuum
}

---
Example – State fault
Example – State fault
state fault{
entry{
strcpy(CurrentState,”Vacuum Fault”);
pvPut(CurrentState);
}
}

---
Building an SNL program
Building an SNL program
Use editor to build the source file. File name must end with
“.st” or “.stt”, e.g. “example.st”
“make” automates these steps:
  - Runs the C preprocessor on “.st” files, but not on “.stt” files.
  - Compiles the state program with SNC to produce C code:
    - snc example.st -> example.c
  - Compiles the resulting C code with the C compiler:
  - cc example.c -> example.o
  - The object file "example.o” becomes part of the application library, ready to be linked into an IOC binary.
  - The executable file “example” can be created instead.

---
Run Time Sequencer
Run Time Sequencer
The sequencer executes the state program
It is implemented as an event-driven application; no polling is needed
Each state set becomes an operating system thread
The sequencer manages connections to database channels through Channel Access
It provides support for channel access get, put, and monitor operations
It supports asynchronous execution of delays, event flag, pv put and pv get functions
Only one copy of the sequencer code is required to run multiple programs
Commands are provided to display information about the state programs currently executing

---
Executing a State Program – IOC
Executing a State Program
From an IOC console
On vxWorks:
  - seq &vacuum_control
On other operating systems:
  - seq vacuum_control
To stop the program
  - seqStop “vacuum_control”

---
Debugging
Debugging
Use the sequencer's query commands:
  - seqShow
    - displays information on all running state programs
  - seqShow vacuum_control
    - displays detailed information on program
  - seqChanShow vacuum_control
  - displays information on all channels
  - seqChanShow vacuum_control,”-”
    - displays information on all disconnected channels

---
Debugging (continued)
Debugging (continued)
Use printf functions to print to the console
  - printf("Here I am in state xyz \n");
Put strings to pvs
  - sprintf(seqMsg1, "Here I am in state xyz");
  - pvPut(seqMsg1);
On vxWorks you can reload and restart
  - seqStop vacuum_control
  - ... edit, recompile ...
  - ld < example.o
  - seq &vacuum_control

---
Debugging - seqShow
Debugging – seqShow
epics> seqShow
Program Name Thread ID Thread Name SS Name
stabilizer ede78 stabilizer stabilizerSS1
beamTrajectory db360 beamTrajectory bpmTrajectorySS
autoControl ed620 autoControl autoCtlSS

---
Debugging – seqShow
epics> seqShow stabilizer
State Program: "stabilizer"
 initial thread id = ede78
 thread priority = 50
 number of state sets = 1
 number of syncQ queues = 0
 number of channels = 3
 number of channels assigned = 3
 number of channels connected = 3
 options: async=0, debug=0, newef=1, reent=0, conn=1, main=0
 State Set: "stabilizerSS1"
 thread name = stabilizer; thread id = 974456 = 0xede78
 First state = "init"
 Current state = "waitForEnable"
 Previous state = "init"
 Elapsed time since state was entered = 88.8 seconds

---
Debugging - seqChanShow
Debugging – seqChanShow
epics> seqChanShow stabilizer
State Program: "stabilizer"
Number of channels=3
#1 of 3:
Channel name: "stabilizerC"
 Unexpanded (assigned) name: "stabilizerC"
 Variable name: "enableButton"
   address = 154120 = 0x25a08
   type = short
   count = 1
 Value = 0
 Monitor flag = 1
   Monitored
 Assigned
 Connected
 Get not completed or no get issued
 Put not completed or no put issued
 Status = 17
 Severity = 3
 Message =
 Time stamp = <undefined>
Next? ( skip count)

---
Additional Features
Additional Features
Connection management:
  - when (pvConnectCount() != pvChannelCount())
  - when (pvConnected(Vin))
Macros:
  - assign Vout to "{unit}:OutputV";
  - must use the +r compiler options for this if more than one copy of the sequence is running on the same ioc
  - seq &example, "unit=HV01"
Some common SNC program options:
  - +r make program reentrant (default is -r)
  - -c don't wait for all channel connections (default is +c)
  - +a asynchronous pvGet() (default is -a)
  - -w don't print compiler warnings (default is +w)

---
Additional Features (continued)
Additional Features (continued)
Access to channel alarm status and severity:
  - pvStatus(var_name)
  - pvSeverity(var_name)
Queued monitors save CA monitor events in a queue in the order they come in, rather than discarding older values when the program is busy
  - syncQ var_name to event_flag_name [queue_length]
  - pvGetQ(var_name)
    - removes oldest value from variables monitor queue. Remains true until queue is empty.
  - pvFreeQ(var_name)

---
Advantages
Advantages of SNL
Can implement complicated algorithms
Can stop, reload, restart a sequence program without rebooting
Interact with the operator through string records and mbbo records
C code can be embedded as part of the sequence
All Channel Access details are taken care of for you
File access can be implemented as part of the sequence

---
When to use the sequencer
When to use the sequencer
For sequencing complex events
E.g. parking and unparking a telescope mirror
Photograph courtesy of the Gemini Telescopes project

---
Should I Use the Sequencer?
Should I Use the Sequencer?
START
CAN I DO THIS IN A DB?
Y
N
CAN I DO THIS IN A DB?
Y
N
USE THE SEQUENCER
USE A DATABASE
END

---
Acknowledgements
Acknowledgments
Slides for this presentation have been taken from talks prepared by the following people
  - Bob Dalesio (LANL/SNS/LCLS)
  - Deb Kerstiens (LANL)
  - Rozelle Wright (LANL)
  - Ned Arnold (Argonne)
  - John Maclean (Argonne)