Title
Finding, Deploying and Managing
EPICS I/O Support
Andrew Johnson, APS

---
Outline
Outline
Meaning of I/O Support
Review of IOC development environment
Development areas as components
Distinguishing Support Modules and IOC Applications
Managing change in Support and IOC top areas
Different ways to support I/O devices
Finding existing software
Deploying support modules
  - Installing software
  - Using it in an IOC

---
I/O Support
Meaning of “I/O support”
Software that connects one or more record types to some real hardware
  - At minimum contains device support code
  - May include record or driver support as well
  - Also covers any additional software needed by those layers
    - Not necessarily EPICS-specific code
May comprise multiple separate software packages, e.g.:
  - drvIpac	Octal232 serial port support
  - Asyn	Serial interfacing software
  - Device Support	Specific commands for the target serial device
Might provide database templates, SNL programs and MEDM screens
  - SynApps does this for beamline devices
  - Not appropriate for all kinds of I/O

---
<top>
IOC Development Environment Review
<top>
  - configure
    - RELEASE
    - CONFIG
    - Other build-system files
  - xxxApp
    - src
      - C & SNL sources, .dbd files
    - Db
      - .db files, templates & substitutions
  - IocBoot
    - Iocxxxx
    - st.cmd
  - Installation directories:
    - dbd, db, include, bin/<arch>, lib/<arch>

---
Components
Development Areas as Components
The <top> structure and Makefile rules are designed to encourage modularity
  - An IOC is built up out of many components
    - Channel access, database access, scanning, other core libraries
    - Record, device & driver support
    - Databases
    - Sequence programs
    - Etc.
  - Components do not have to be defined in the same <top> as the IOC itself
    - Most of the IOC software comes from Base
    - Other <top> areas can provide additional components
    - Other <top> areas can override (replace) components from Base
The configure/RELEASE file determines what other <top> areas will be searched for required components, and in what order
  - Only the installation directories of other <top> areas are searched

---
Support vs IOC
Support Modules vs. IOC Applications
Most sites distinguish between <top> areas that provide commonly-used components, and those that build IOCs
  - Record, Device and driver support are usually shared by many IOCs
  - Having multiple copies of source files is a recipe for disaster
  - Different engineers maintain device support than IOCs
  - The life-cycles of the two are usually very different
Areas that provide components are Support Modules
  - /usr/local/epics/R3.14.6/modules/...
Areas that build IOCs are IOC Applications
  - /usr/local/epics/R3.14.6/ioc/...
IOC areas use entries in configure/RELEASE to indicate which support apps they will use components from
IOC areas may contain local record/device/driver support, but only for hardware that is not used in in any other IOC subsystem

---
Change: Support
Managing Change: Support Modules
Support modules usually only change when a bug is fixed, or some new functionality is added
  - It should be a deliberate decision by the engineer responsible for an IOC or subsystem to use a new version of a support module
    - Bug fixes can introduce new bugs elsewhere
    - New functionality might include changes that break old applications
Therefore: once installed and in use by an operational IOC application, a support module’s <top> area should never be changed
  - New versions of the module should be installed alongside the old one
  - The engineer responsible for an IOC subsystem can switch to the new version when s/he is ready for it by changing the IOC Application's <top>/configure/RELEASE file to point to the new version
  - The old version is not deleted until it will never be required again
    - It’s easy to revert to a previous version if problems are found
    - Disk space is cheap
Sites should document what changed in each update of a support module, and should notify IOC engineers that a new version is available

---
Change: IOC
Managing Change: IOC Applications
IOC applications change very frequently in small ways
  - Updating alarm limits, revised sequences, adding new I/O points etc.
It should be relatively easy to modify the files that configure an IOC (databases, subroutines, sequence programs etc.)
  - Elaborate version control procedures make it harder to respond to change requests, so less change will happen or the procedures get ignored
However it is important to retain the history of what application changes were made, when and by whom
  - Being able to quickly back out of recent modifications can be essential to recovering from incorrect changes
This is very different to the requirements of managing a support application
  - Do not attempt to use the same approach to manage both

---
Ways to support
Ways to support I/O devices
Hardware-specific device and/or record support
  - Best solution if already available
  - Recommended if there will be multiple instances
    - Communications protocol can be hidden from users and usually from EPICS applications developers
    - Much easier to handle any device peculiarities
  - May be essential for complex devices
Generic support
  - Available for general-purpose bus, serial, and network connected I/O
  - Device-specific knowledge is contained in database records
    - Special fields in a custom record
    - Parm field of a hardware link address
  - Not possible for complex devices or protocols

---
Finding
Finding existing software
Supported Hardware database on EPICS website
EPICS Collaboration meetings
Tech-talk mailing list
  - Search the archives before asking
Google Search
Most existing support software is for R3.13.x on vxWorks
Porting to R3.14 is relatively easy
Porting to RTEMS is slightly harder
  - Should be straight-forward if the software uses devLib
Porting to Linux is inadvisable for VME or PCI-based hardware
  - Linux Kernel drivers are hard to write and debug
Serial or network-based support can be made as portable as Base
  - The Asyn framework simplifies this process

---
Deploying
Deploying EPICS Support modules
Installing the software
  - If installation instructions are provided, read & follow them!
    - SynApps users should read the synApps README file
      - The synApps configuration system is slightly different
  - Prerequisites:
    - EPICS Base R3.14.x built for the desired architecture(s)
    - All other support modules needed have already been built

---
Configure
Deploying: Configure the module
Extract the source file to the required location using tar/unzip/...
Edit the configure/RELEASE file
  - Set the EPICS_BASE variable pointing to the Base directory
    - EPICS_BASE=/usr/local/epics/R3.14.6/base
  - Set any other required paths in the file as appropriate, e.g.:
    - IPAC=/usr/local/epics/R3.14.6/drvIpac-2.7
      ASYN=/usr/local/epics/R3.14.6/asyn-3.3
  - You may define other variables and use the Makefile $(variable) syntax
    - SUPPORT=/usr/local/epics/R3.14.6
      EPICS_BASE=$(SUPPORT)/base
      IPAC=$(SUPPORT)/drvIpac-2.7
      ASYN=$(SUPPORT)/asyn-3.3
  - Variables that name other support modules must expand to absolute pathnames beginning with a '/'; relative paths will not work
    - '..' is allowed as a component within an absolute path

---
Build
Deploying: Build the module
Run GNU make in the <top> directory
  - To simultaneously log the output to a file, use these commands
    - csh,tcsh: gnumake |& tee build.out
    - sh,ksh,bash: gnumake 2>&1 | tee build.out
  - This checks the configure/RELEASE file for consistency with the support modules named, and generates files in configure/O.<arch>
  - Then it descends through the other subdirectories of <top>, compiling and installing products as necessary

---
Using
Using Support in an IOC Application
Mostly very specific to the Support Module
General steps are
  - Add a line to the IOC Application's configure/RELEASE file that points to the new module's <top> directory
    - ASYN=$(SUPPORT)/asyn-3.3
  - Edit the Makefile where the IOC is built
    - Add a line for each library to be linked against
      - example_LIBS += asyn
    - Add a line for any .dbd files to be included
      - example_DBD += asyn.dbd
    - Alternatively this might become a line in exampleInclude.dbd:
      - include "asyn.dbd"
  - Add any necessary lines to the st.cmd file
  - Create record instances, instantiate templates, etc.
  - Rebuild the IOC Application from <top>
    - gnumake rebuild