## Slide 1: Scan System: Experiment Automation
Kay Kasemir,
Xihui Chen
RAL EPICS Meeting, May 2013

## Slide 2: Scope
Automate the experiment
  “Scan” = Sequence of commands
  Interact via Channel Access (pvManager)
  Start/stop/monitor a long-running sequence
Not:
  Closed-loop control
  Data acquisition
  Data analysis

## Slide 3: Should be Easy
GUI:
… or script:
Robust execution
Monitor, pause, resume, abort
Open Shutter
Wait for certain beam charge to accumulate
Step motor
X += 1
X < 10 ?
No
Yes
Set motor X = 0
Close Shutter

## Slide 4: BOY Example
1. Configure
2. Start
3. Monitor

## Slide 5: Tabular OPI

## Slide 6: Neutron Imaging Beamline ORNL HFIR CG-1D
First EPICS/CSS operation with beam, Jan. 8, 2013
Scans

## Slide 7: Scan Monitor
List Scans on Server
  Idle: To be executed next
  Running: With progress report
  Finished, Failed: Past runs

## Slide 8: Scan Plot
Plot variables used by scan
Get data from Running or Finished scans
Not data acquisition! Just another way to monitor progress of scan.

## Slide 9: Scan Editor
Add commands
Set parameters
Open, save
Drag/drop commands or PV names (also as XML text)
“Undo”
Device PVs (or alias) can be picked from beamline-specific configuration

## Slide 10: Scan Commands
Set
  Set device (PV) to a value.
  Optional wait for read-back, same or other PV, with timeout.
Wait
  Wait until a device (PV) reaches a certain value. Support condition: >, <, ==, >=, <=, increment-by, decrease-by. Optional timeout.
Loop
  Command that performs a loop, optional read-back and timeout.
Log
  Log data for plot in addition to variables used by Set, Wait, Loop
Delay
  Delay for a certain time. Discouraged. Use Wait.
Script
  Execute jython code. Use with care.
Custom commands can be added via Eclipse extension points.

## Slide 11: Simulation Mode
Simulated PV changes
Estimates times

## Slide 12: Monitor, Adjust Live Scan
Active Command
Scan Info
Adjust properties
of live scan

## Slide 13: Scripted Scan
… or use ‘vi’, shell:
from scan_client import * help(scan) scan('Demo', ('xpos', 1, 10))
Jython editor, debugger
Jython console

## Slide 14: Matlab
Create Scan
Monitor
Analyze
(maybe submit follow-up scan)

## Slide 15: Web Interface Prototype

## Slide 16: Scan Server
Submitted scans are queued for execution
  Pre- and Post-Scan commands: open/close shutter, …
CSS/Eclipse ‘headless’ application
‘PV’: EPICS, simulated
  Alias names for PVs as well as plain PV names
Telnet interface: Status, pause, resume, …
Java RMI interface: Submit, status, pause, resume, get data, …
  Scans transferred in XML format
  RMI = Java, Jython, Matlab, Scala, JRuby, …
Web Interface
  REST

## Slide 17: Overall Picture for SNS
Nexus
Nexus
Sample Environment Equipments
Sample Environment Equipments
Sample Environment
Detector
Instrument Events
Aggregator
Translation Service
Mantid
Nexus
Histogram
Service
Data Stream
GUI: CSS
GUI: CSS
GUI: CSS
EPICS IOCs
Scan Server
Channel Access

## Slide 18: Summary: Experiment Automation Building Block

## Slide 20: Experiment Control for EPICS
Sample Environment Equipments
Sample Environment Equipments
Sample Environment Equipment
GUI: CSS
Jython, Matlab, …
EPICS IOCs
Scan Server
Channel Access

## Slide 21: EPICS Sequencer?
Compile, link, …
No GUI
No progress, pause, resume
Can do anything
Excellent for “permanent” automation, not for changing scan scenarios

## Slide 22: Scripts (Python, Jython, Scala, …)
No progress, pause, resume
Can do most anything
“Works”, but…

## Slide 23: Allow Anything = Robust
set(setpoint, 30); # Assume OK after 10 seconds wait(10.0);
set(nonexisting_channel, 42);
while (readback < 10) { /* busy loop */ }
set(setpoint, 30); # Wait for readback to match waitForValue(readback, 30);
if (notConnected(…)) reportError(); while (readback < 10) { sleep(1); if (timeout_exceeded) reportError(); }

## Slide 24: APS “Scan Engine”
Claude Saunders, Mitch McCuiston, Brian Tieman, Tim Mooney
“Scan Engine” executes submitted scans
Scan = List of robust commands
Scan System adds
“Loop” command
Pause, Resume
CSS PV instead of new PV layer
Tight CSS GUI integration AND basic script access

## Slide 25: Performance
Command Execution
  80000 commands/second: Delay 0 sec, Set w/o read-back
  4500 commands/second: Set w/ read-back, Loop
Download scan into Editor
  10000 commands: 1 second
  50000 commands: 15 seconds

## Slide 26: Beam Line Configuration
Required (soft) IOCs
  Used by separate tools to start/stop as required
Scan System Aliases
  Available within scans
Simulation Info
  Slew rates
DAQ info
  Which channels to log with neutron data?