## Slide 1: Redundant IOC improvements by LANL
Goal: Rather than 2 IOCs talking on the same bus, as at DESY. We want to command redundant hardware as part of our new master timer system.
Improvements that may be useful for everyone:
Added support for syncing field with SPC_DBADDR (waveform records)
  Modified the Continuous Control Executive (CCEXEC) to support larger fields.
Made it possible to specify which records should be synced
  Configurable via info nodes.
  Modified e2db so that CapFast can be used to configure info nodes.

## Slide 2: Redundant hardware specific improvements
Added an option to only pause the channel access server instead of the entire IOC.
Call post_event on the slave when the database becomes synced with the master (CCEXEC_SLV_INSYNC state) so that passive records can be made to process on the slave.
  Uses event-driven fanout records.
  Can control the processing order.
  Particularly useful for commands.